## Slide 1
Memory-Access-Aware Loop Transformations of Accelerator-Bound OpenMP Loops
Artem Chikin1, Taylor Lloyd1, José Nelson Amaral1, Ettore Tiotto2
1University of Alberta 2IBM Canada
Portable Performance Demands Stronger Program Analyses
Memory Access Effects
A collapsed nest’s combined iteration space changes which threads execute which iteration points, affecting memory access patterns.
Parallelism Effects
Collapsing a loop nest with a parallel outer loop increases the overall number of iterations that can execute in parallel.
Performance
Takeaway
Architecture-aware compilers must employ strong program analyses to generate higher-performing code without portability-reducing annotations.
OpenMP supports architecture-agnostic accelerator programming. Computation on CPUs and GPUs has opposing performance demands to memory access patterns. CPUs must avoid false-sharing and achieve per-thread spatial locality. GPUs demand memory coalescing:
Portability
IPAD-enabled safety and profitability analyses power transformations that improve performance:
Iteration-Point Algebraic Difference (IPAD): A sophisticated static analysis framework that computes the inter-iteration memory access stride by calculating differences of addressing expressions’ symbolic values that capture both data and control flow:
IPAD analysis framework can automatically discover optimization opportunities that would otherwise have to be specified by the programmer, like collapse(n).
SPEC ACCEL: 557.pcsp
*High-throughput benchmark versions used
*
Polybench